## Slide 1: 2025 NTU Computer Vision Final Project Iris Recognition Challenge
Ganzin Technology, Inc.
見臻科技

## Slide 2: Human Eye Anatomy
Pupil
Iris

## Slide 3: Iris Recognition
Unique: Iris variability among different people is enormous
  Even from two eyes of the same person or eyes of twins
  Large inter-class distance
Stable: Iris is stable over lifetime
  Iris begins to form in the third month of gestation and the structures are largely complete by the eighth month
  Small intra-class distance
Contactless: Easy to capture iris images
  Iris recognition is more hygienic than biometrics that requires contact, such as fingerprint recognition.
Safe: Iris is well protected by eyelids and hard to forge

## Slide 4: How Iris Recognition Works
Typical pipeline
Daugman’s rubber sheet model
An example of good feature selection

## Slide 5: How Iris Recognition Works
Deep learning based methods
Input: iris ROI
Input: polar transformed iris

## Slide 6: Challenges in AR/VR Devices
Eye camera has tilted viewing angle

## Slide 7: Common Evaluation Metrics
False acceptance rate (FAR)
False rejection rate (FRR)

## Slide 8: Common Evaluation Metrics
Discriminability index (d’ score)
  See RMS sd discriminability index in wiki

## Slide 9: Evaluation
Evaluation protocol
eval.py
Your algorithm
Image 1
Image 2
Dissimilarity 0~1
0: genuine
1: imposter
Sample image pairs from dataset
Compute d’ scores
Described in a txt file
What ever the original output range is, normalize it to 0~1
dataset/Ganzin-J7EF-Gaze/001/L/view_3_1.png, dataset/Ganzin-J7EF-Gaze/001/L/view_3_2.png, 0.013
dataset/Ganzin-J7EF-Gaze/001/L/view_3_1.png, dataset/Ganzin-J7EF-Gaze/001/L/view_3_3.png, 0.010
dataset/Ganzin-J7EF-Gaze/001/L/view_3_1.png, dataset/Ganzin-J7EF-Gaze/002/L/view_3_1.png, 0.996
dataset/Ganzin-J7EF-Gaze/001/L/view_3_1.png, dataset/Ganzin-J7EF-Gaze/003/L/view_3_1.png, 0.996
Format: img1 path, img2 path, score

## Slide 10: Dataset
CASIA-Iris-Thousand
  20,000 NIR images of size 480x640 captured from 1,000 subjects
  000~199 as test set
CASIA-Iris-Lamp
  16,212 images of size 480x640 captured from 411 subjects
  001~080 as test set
CASIA-Iris-Lamp collection
CASIA-Iris-Thousand images are collected with IKEMB-100 camera
Notes: In practice, it is difficult to obtain ground truth pupils

## Slide 11: Dataset
Ganzin-J7EF-Gaze
  Collected by J7EF-Gaze
  10 subjects
  Left/right eyes
  5 eye directions
  10 images per eye direction
  10 * 2 * 5 * 10 = 1,000 images
Test set
  Left eye viewing angle 3
  Right eye viewing angle 2
view_1_1.png
First number: viewing angle index
Second number: image index
Notes: In practice, it is difficult to obtain ground truth pupils

## Slide 12
001 left eye

## Slide 13
001 right eye

## Slide 14: Iris Segmentation
You may use off-the-shelf models for segmentation
  IrisParseNet
  RITNet
  EllSeg
  etc.
Semantic segmentation by RITNet

## Slide 15: Open-source Iris Recognition Repositories
It is allowed to start with an open-source repositories
  OpenSourceIrisRecognition
  Open-IRIS
  Dynamic graph representation for partially occluded biometrics (TPAMI 2023)
  etc.
Visualization of iris codes computed by Open-IRIS

## Slide 16: Other Requirements
Single algorithm for all datasets
  You may have different models for different datasets
  You may also tune parameters for different datasets

## Slide 17: Scoring
Performance 60%
  CASIA-Iris-Thousand (20%)
  CASIA-Iris-Lamp (20%)
  Ganzin-J7EF-Gaze
    Left eye direction 3 (10%)
    Right eye direction 2 (10%)
Report 40%
Bonus 10%
  Ganzin-J7EF-Gaze
    Cross angle matching

## Slide 18: Reference
John Daugman. "How Iris Recognition Works." IEEE Transactions on Circuits and Systems for Video Technology 14.1 (2004): 21.
Jasem Rahman Malgheet, Noridayu Bt Manshor, and Lilly Suriani Affendey. "Iris recognition development techniques: a comprehensive review." Complexity 2021.1 (2021): 6641247.